## Slide 1: Predictive Maintenance System for Water Pipelines
Team Innovexa
Sukirtha Shree R
Thiruvenpha T
Jeevadharshini L
Kiruba Shamili

## Slide 2: Predictive Maintenance System for Water Pipelines
Team Innovexa
Sukirtha Shree R
Thiruvenpha T
Jeevadharshini L
Kiruba Shamili

## Slide 3: Predictive Maintenance System for Water Pipelines
Innovexa
Problem Statement
Solution
Existing systems detect leaks, but we need a predictive solution to monitor pipeline health and prevent failures, leaks, contamination, and structural damage before they occur.
A multi-sensor predictive maintenance system using IoT sensors (Pressure, Flow, Vibration, Temperature, Water Quality), MySQL for data storage, ML algorithms for failure prediction, and real-time alerts via Twilio SMS and mobile app notifications.
Emergency!
Leak detected

## Slide 4: System Architecture
Emergency!
Leak detected
ESP32 Microcontroller
Collects sensor data
MySQL Database
Stores real-time data.
Machine Learning Model (LSTM & Autoencoder)
Predicts failures.
Mobile App
Alerts users.
Monitors pipeline health
Predictive Maintenance System for Water Pipelines
Innovexa

## Slide 5: Hardware Components
Predictive Maintenance System for Water Pipelines
Innovexa

## Slide 6: Hardware Components
Predictive Maintenance System for Water Pipelines
Innovexa
ESP32
(WiFi-enabled microcontroller)
Acts as the central processing unit, collecting data from all sensors.
Enables wireless communication to send data to the cloud or a local server for analysis.

## Slide 7: Hardware Components
Predictive Maintenance System for Water Pipelines
Innovexa
Sensors
Pressure Sensor (MPX5700AP)
Detects pressure fluctuations.
Water Flow Sensor(YF-S201)
Measures flow rate changes.
Vibration Sensor (SW-420)
Detects unusual vibrations (pipe cracks).
Temperature Sensor (DS18B20)
Monitors pipe overheating risks.
Water Quality Sensor (TDS Sensor)
Detects contamination.

## Slide 8: Hardware Components
Predictive Maintenance System for Water Pipelines
Innovexa
Power Supply & Jumper Wires
Provides stable power to the ESP32 and sensors.
Ensures seamless connectivity and data transmission between components.

## Slide 9: Software Components
Predictive Maintenance System for Water Pipelines
Innovexa

## Slide 10: Software Components
Predictive Maintenance System for Water Pipelines
Innovexa
Embedded System (ESP32 Code)
Arduino IDE (C++)
HTTP Client for API communication
Backend (Flask API)
Python (Flask, MySQL Connector, Twilio API)

## Slide 11: Software Components
Predictive Maintenance System for Water Pipelines
Innovexa
Database
MySQL(Stores sensor data)
Machine Learning
LSTM + Autoencoder

## Slide 12: Software Components
Predictive Maintenance System for Water Pipelines
Innovexa
Mobile App
Flutter / React Native(Real-time monitoring & alerts)
Notification System
Twilio SMS API
Firebase Cloud Messaging (FCM) for mobile app

## Slide 13: AI-Powered Machine Learning Model
B
Why?
Learns pipeline behavior over time, improving failure prediction accuracy.
A
Model Used:
LSTM (Long Short-Term Memory) + Autoencoder for Anomaly Detection
C
Data Inputs
Pressure (<4.0 = Normal, >4.5 = Leak Risk)
Flow Rate (Unusual flow drop = Leakage)
Vibration (High vibrations indicate cracks)
Temperature (Overheating = Pipe burst risk)
Water Quality (Contamination suggests pipeline damage)
Predictive Maintenance System for Water Pipelines
Innovexa

## Slide 14: MySQL Database Structure
Predictive Maintenance System for Water Pipelines
Innovexa

## Slide 15: Alert & Notification System
Twilio SMS Alert
Sends instant SMS alerts to the maintenance team when sensor values indicate a failure risk.
Ensures quick response to prevent pipeline damage or leaks.
Data Stored in MySQL
Logs all sensor data and alerts in a MySQL database for future analysis.
Enables tracking of pipeline health trends and improving predictive accuracy.
Mobile App Push Notification 📱 (via Firebase)
Sends real-time push notifications to the mobile app for immediate attention.
Provides detailed alerts with sensor data and risk level for better decision-making.
Predictive Maintenance System for Water Pipelines
Innovexa

## Slide 16: Mobile App Features
C
Maintenance Report
View pipeline health history.
D
Predictive Alerts
AI-driven insights for proactive maintenance.
B
Notification System
Alerts users about potential failures.
A
Dashboard
Displays real-time sensor readings.
Predictive Maintenance System for Water Pipelines
Innovexa

## Slide 17: Advantages & Future Scope
Advanatges
AI-Powered Prediction → Reduces Maintenance Costs
Multi-Sensor Approach → Higher Accuracy
Real-Time Alerts → Faster Response
Scalable → Smart Cities & Rural Deployments
01
Future Enhancements
AI-Driven Self-Healing Pipelines – Autonomous leak control.
GIS Mapping – Location-based maintenance analytics.
Blockchain for Secure Data Logging – Prevents tampering.
02
Predictive Maintenance System for Water Pipelines
Innovexa

## Slide 18: Conclusion
Developed a Predictive Pipeline Maintenance System using ESP32, ML & IoT sensors.
Real-time monitoring + AI-powered alerts improves maintenance efficiency.
Potential Impact: Can be scaled for municipalities, industries, and rural water management.
Predictive Maintenance System for Water Pipelines
Innovexa

## Slide 19
THANK YOU
Predictive Maintenance System for Water Pipelines
Innovexa